Functions in GCERlib2015 (updated last on April 24)

driveTrain
void describe_driveTrain(NARmotor leftw, NARmotor rightw, int diameter);
Saves user entered data into the driveTrain structure. Must be called before using the	camera, tophat_drive, et_drive, or driveTrain functions.

int convert_mm_ticks(int millimeters);

void driveTrain_move_ticks(int velocity, int ticks);

void driveTrain_move_mm(int velocity, int millimeters);

void driveTrain_accel_ticks(int v_initial, int v_final, int ticks);

void driveTrain_accel_mm(int v_initial, int v_final, int millimeters);

void driveTrain_spin_angle(int velocity, int angle);

camera
example code:
camera scheme1 = create_camera_scheme(0, 0, 20);
...ending setup...
camera_align_x(scheme1, 80, 500);

camera create_camera_scheme(int channel, int object_count, int pixels_of_error);
Must be called before using any of the other camera functions

void camera_set_x(camera camera_properties, int x_coordinate);
Sets the desired x_coordinate for the next call to camera_align(cameraName, velocity);

void camera_set_y(camera camera_properties, int y_coordinate);
Sets the desired y_coordinate for the next call to camera_align(cameraName, velocity);

void camera_calibrate_position(camera camera_properties);
Sets the desired x and y coordinates based off of the object seen by the camera.

void camera_set_object_count(camera camera_properties, int object_count);
Sets the object count for the specified camera scheme.

void camera_align_x(camera camera_properties, int x_coordinate, int velocity);

void camera_align_y(camera camera_properties, int y_coordinate, int velocity);

void camera_align(camera camera_properties, int velocity);//not finished

tophat_drive
void tophat_calibrate(int right_port, int left_port);
Guides user through process of setting calibrating the tophats. Must be called before other tophat_drive functions.

void tophat_drive_follow_left(...);//not finished

void tophat_drive_follow_right(...);//not finished

void tophat_align_black(int velocity);

void tophat_align_white(int velocity);

et_drive
void describe_et_drive(int head_port, int tail_port, int head_per_5mm, int tail_per_5mm);
Saves specified data concerning the et driveTrain. Must be called before using other et_drive functions.

void et_drive_follow(int ticks_per_second);//not finished
Follows wall using the two et sensors previously described.

void et_drive_align(int ticks_per_second);//not finished
Aligns on wall using the two er sensors previously described.

et
Example code:
NARet et1 = create_et(4, 465);
et_get_mm(et1);

NARet create_et(int port, int range_per_5mm);

float et_get_mm(NARet etName);

create_drive
float create_get_charge();

void create_drive_segment(int speed, int distance_mm);

void create_spin(int velocity);

void create_spin_angle(int speed, int angle);

void create_wait_for_bump(int velocity);

servo
Example code:
servo arm = create_servo(0, 0.4);
servo_spin_angle(arm, 90);

servo create_servo(int port, float ticks_per_millisecond);
Creates a servo object and saves specified data to it.

void servo_spin_ticks(servo servo_properties, int ticks);

void servo_spin_angle(servo servo_properties, int angle);

void servo_set_tpms(servo servo_properties, float tpms);
sets the ticks_per_millisecond of the specified servo to specified number.

motor
Example code:
NARmotor motor1 = create_motor(0, 52, 880);
motor_move_mm(motor1, 56.5, 0.4);

NARmotor create_motor(int port, int diameter, int ticks_per_cycle);

float motor_convert_ticks_mm(int ticks);

void motor_move_mm(motor motorName, float mm, int ticks_per_second);